Flume experiments on the initiation and evolution of transverse bedforms

Paul Jarvis and Nathalie Vriend
DAMTP, University of Cambridge

At first sight, aeolian and aqueous dunes are distinct as the medium changes from air to water. However, key dynamical dimensionless parameters are comparable and the physical behaviour of interacting aqueous dunes may be extrapolated to describe aeolian systems.

We study the formation and evolution of transverse dunes in a thin, large-diameter annular flume of diameter 1 m, height 30 cm, and gap thickness 7.5 cm, filled with granular material (sand/ballotini) and water. A shear flow, created by a rotating table and fixed paddles, is exerted on a bed with two initial conditions: a horizontal flat bed or pre-formed variable-sized mounds of sediment. The flat bed experiments probe the initial destabilisation of the bed, the creation of ripples, and the resultant coarsening of the bed profile as ripples coalesce to form larger dunes. The second set of experiments examines the interaction between colliding pairs of dunes of variable sizes.